## Slide 1: Warehouse and Distribution Science
Chapters 7 & 8
Layout of
A Carton-Pick-From-Pallet Area
And
A piece-pick-from-carton area

## Slide 2: Carton-Pick-From-Pallet Area
Low pick density means lost of traveling for order picking cases
Cases picked onto pallet jack or conveyor
Fast movers typically stored in floor storage or bottom level of pallet rack

## Slide 3: Carton Picking from Pallet Rack
Cartons are picked from the bottom (dedicated), most convenient level; when the bottom position is empty, a restocker refills it by dripping a pallet from above. Newly arriving pallets are inserted into the high overstock area (randomly).

## Slide 4: Forward-Pick Areas
Some skus may go into a forward-pick or fast-pick area that is more convenient to pick, but space is limited
Forward pick locations are dedicated to a sku
Which skus to put in forward-pick area?

## Slide 5: Notation
Symbol | Definition | Source
li | Min practical number of locations for sku i | Determination based on stockout & congestion
ui | Number of forward pick locations to store “all on-hand pallets” of sku i | Historical data
pi | Number of picks for less-than-pallet qtys | 
di | Number of pallets moved to replenish less-than-pallet picks | 
Di | Number of pallets moved in full-pallet picks | 
s | Minutes saved by pick from forward area vs bulk area | 
cr | Minutes to restock forward pick area | 
c1 | Minutes for pick from forward area | 
c2 | Minutes for pick from bulk area | 

## Slide 6
Example 7.2
Labor efficiency = (savings for forward pick vs bulk) – (cost to replenish)
Sku A has the strongest claim to storage in the fastpick area because it is estimated to generate the greatest labor savings per forward location.
Sku | Picks/year | Demand (plts/yr) | li | Labor Efficiency
A | 600 | 20 | 3 | ((1)(600)-(3)(20))/3=180
B | 1000 | 100 | 5 | ((1)(1000)-(3)(100))/5=140
C | 200 | 2 | 2 | ((1)(200)-(3)(2))/2=97

## Slide 7: Figure 7.4
Skus ranked by labor efficiency.
Only about the top 100 skus would save labor if picked from the forward area.
The next 400 may or may not be picked from forward area, without much affect on labor cost either way.
The bottom 100 skus would be uneconomical to pick from forward area.

## Slide 8: Picking Pieces-from-Carton
Most labor intensive activity in the warehouse
More prevalent today as pressures for companies to reduce inventories and move toward 1-piece-flow

## Slide 9: Basic issues for Fast-Pick Area
Which skus to store in the fast-pick area?
How much of each sku to store there?
Methods
  Fluid model
  Slotting

## Slide 10: Multiple Fast-Pick Areas

## Slide 11: Figure 8.8
Example of slotting that accounts for the geometry of the skus and the storage mode.
This pattern of storage minimized total pick and restock cost for this set of skus and this arrangement of shelves.
The software reports the percentage of picks from this bay on each shelf.
This was produced with the slotting software written by Bartholdi & Hackman

## Slide 12
Changing the cost-per-restock is economically equivalent to changing the volume of the fast-pick area… it is better to reduce the restock cost because increasing the size of the fast-pick area increases the average cost per pick